Plan Commission Staff Report						             May 21, 2019

Department of Planning and Building

Town of McCordsville

Project:		PC-19-004, Oakcrest

Petitioner: 		Pulte Group

Request:	Petitioner is seeking approval of the Development Plan and Secondary Plat for the Oakcrest residential subdivision

Staff Review:	Oakcrest is a fifty-five (55) lot section on approximately 25 acres.  This neighborhood is located immediately along the east side of CR 700W, south of CR 900N.

Subject Property Zoning

The property is zoned Oakcrest PUD.

Surrounding Land-uses & Zoning

The subject Real Estate is currently undeveloped.  The surrounding land uses are as follows:

- North: Single-family homes and Geist Community Church

- East: Single-family homes in the Deer Crossing neighborhood

- South: Single-family homes in the Deer Crossing neighborhood

- West: Residential lots in Marion County

Infrastructure

All lots will be accessed through the internal public streets.  In accordance with the preliminary plan, the project will install a stub street to the north for future connectivity.  Two stormwater detention facilities will be constructed with this neighborhood in accordance with the master drainage plan.  Sanitary sewer service will be provided by the Town, and water service will be provided by Citizen’s Energy Group.

Development Standards

The Oakcrest PUD includes its own Development Standards:

Setbacks (all minimums):

Parcel D:	FY:  25’

SY:  6’

RY: 25’

Lot Width:  	60’

Lot Size: 	7,800 SF

Living Area: 	1,600 SF (1-story)

1,800 SF (2-story)

Lot Coverage:	45% (multi story)

50% (ranch)

Home Height:	35’

Perimeter Landscaping:  A 50’ wide buffer along CR 700W is required by the PUD.  The buffer must include 7 trees and 6 shrubs per 100 lineal feet, in addition to mounding.  The petitioner’s plans meet this requirement.

Lot Landscaping: Each lot has must include 1 shade tree, 1 evergreen tree, and 12 shrubs.  In addition, sod is required for front yards.  This item is reviewed for after each home is constructed.

Architecture: All homes must comply with the Oakcrest PUD.  All homes will be reviewed on permit by permit basis when submitted for building permit review.

Lot Count: The maximum number of residential units within Oakcrest is limited to 55.  The petitioner’s plans meet this requirement.

Street Lighting: A minimum of four (4) street lights, plus dawn to dusk lights are required by the Oakcrest PUD.  The petitioner’s plans meet this requirement.

Pedestrian Accessibility:  The PUD requires internal sidewalks on the both sides of all internal streets and a perimeter path along CR 700W (including the Scott property).  The petitioner’s plans meet this requirement.

Open Space:  Open Space is required in accordance with the Preliminary Plan.  The petitioner’s plans meet this requirement.

Entrance Median: The PUD requires a median at the entrance.  The petitioner’s plans meet this requirement.

Technical Advisory Committee (TAC)

The project went to TAC on April 4, 2019, and received a number of comments.  All comments applicable to the Plan Commission’s review have been addressed.  The petitioner will continue to work with staff on setting addresses, street names, and stormwater concerns.

Staff Comments:	Staff is supportive of this petition and recommends approval.  Following discussion the Commission can motion to provide (a) approval, (b) continuance, or (c) denial.