Plan Commission Staff Report						             July 20, 2021

Department of Planning and Building

Town of McCordsville

Project:	Preserve at Brookside Development Plan & Secondary Plat

Petitioner: 		Pride Investments

Request:	Petitioner is seeking approval of the Development Plan and Secondary Plat for the Preserve at Brookside.

Staff Review:	This project consists of 98 units in 25 buildings and one adjacent lot for a planned fire station.

Subject Property Zoning

The property is zoned Villages at Brookside PUD.

Surrounding Land-uses & Zoning

The subject Real Estate is currently undeveloped.  The surrounding land uses are as follows:

- North: Single-family homes and the Geist Montessori Academy, all zoned as part of the Bay Creek at Geist PUD

- East: Undeveloped property zoned as part of the Villages at Brookside PUD

- South: Single-family homes developed as part of the Villages at Brookside PUD

- West: An assisted living and senior apartment community zoned as part of the Villages at Brookside PUD

Infrastructure

All lots will be accessed through the internal public streets.  In accordance with the preliminary plan, this section will feature one entrance on CR 900N and an emergency access point connection to the south through Section 2 of the Villages at Brookside.  The project will install a perimeter sidewalk along CR 900N.  Stormwater detention is provided through the Villages at Brookside master drainage plan.  Sanitary sewer service will be provided by the Town, and water service will be provided by Citizen’s Energy Group.

Development Standards

The Amended PUD includes its own Development Standards:

Residential Uses:

FY Setback (along 900N):		50’

FY Setback (along internal streets):	50’

SY Setback:				as shown on concept plan

RY Setback (along south property line):	30’

Min. Building Separation:		as show on the concept plan

Min. Unit Size:				1,400 SF

Max. Primary Structure Height:		35’

Fire Station Uses:

FY Setback (along 900N):		50’

SY Setback (east P.L):			10’

SY Setback (west P.L):			30’

RY Setback:				30’

Max. Primary Structure Height:		40’

Perimeter Landscaping:  A buffer is required along the south property line of the residential area and both the west and south property lines of the fire station area. Such buffer-yards are required to be a minimum of 30’ in width and feature 7 trees and 10 shrubs, and mounding. The petitioner’s plans meet this requirement.

Lot Landscaping: Each unit has must include 3 trees and 12 shrubs, with additional requirements for corner lots, and certain garage protrusions.  In addition, sod is required for front yards.  This item is reviewed for after each home is constructed.

Architecture: All homes must comply with the Amended PUD.  All homes will be reviewed on permit-by-permit basis when submitted for building permit review.

Street Lighting: Street lighting, consistent with the Town’s Zoning Ordinance is required.  The petitioner’s plans meet this requirement.

Pedestrian Accessibility:  The PUD requires internal sidewalks on both sides of all internal streets and a perimeter sidewalk along CR 900N.  The petitioner’s plans meet this requirement.

Open Space:  Open Space is required in accordance with the Preliminary Plan.  The petitioner’s plans are in compliance.

Entrance Median: The PUD requires a median at the entrance.  The petitioner’s plans meet this requirement.

Entrance Signage: The PUD requires primary signage monumentation at the entrance.  The petitioner’s plans show the primary monumentation.

Technical Advisory Committee (TAC)

The project went to TAC on June 3, 2021 and received a number of comments.  Staff is currently wrapping a few final comments with the petitioner.  Those comments are related to the location of a street name sign, ROW dedication, and minimum building separation.  Staff will see that these remaining issues are completed prior to the meeting.  The petitioner will continue to work with staff on setting addresses, street names, and stormwater concerns.

Staff Comments:	Staff is supportive of this petition and following resolution of the items listed above will recommend approval.  Following discussion, the Commission can motion to provide (a) approval, (b) continuance, or (c) denial.